## Slide 1
Objective
Develop improved, open-source models that can simulate the impacts of heat waves on the electric power system
Approach
Characterize derating of power plant capacity and efficiency as functions of ambient temperature
Develop a modified MILP (mixed-integer linear programing) unit commitment formulation that can accommodate hourly deratings
Couple this production cost model with hourly temperature data and a load model to quantify heat wave impacts on grid operations
Quantifying the Impacts of Heat Waves on Power Grid Operation
Production cost difference (one indicator of grid stress) for four cases and four different generator categories (ST=steam turbine, GT=gas turbine, CCGT=combined cycle gas turbine)
Conclusions
Heat wave impacts can be addressed without increasing the dimensionality of the unit commitment problem
Production cost models that do not account for the impact of hourly temperature fluctuations on electricity supply and demand may significantly underestimate the risks associated with heat wave events
Ke X, D Wu, J Rice, M Kintner-Meyer, and N Lu. 2016. “Quantifying the Impacts of Heat Waves on Power Grid Operation.” Applied Energy 183: 504-512. DOI: 10.1016/j.apenergy.2016.08.188
Case 1: no derating
Case 2: capacity derating
Case 3: efficiency derating
Case 4: cap. & eff. derating
Notes: http://www.pnnl.gov/science/highlights/highlights.asp?division=749