## Slide 1: Results of SWAT Model Performance for 111 Studies that Report Simulation of Hydro-Climatic Extremes
Tan, M.-L., P. Gassman, X. Yang and J. Haywood. 2020. A review of SWAT applications, performance and future needs for simulation of hydro-climatic extremes. Advances in Water Resources. 143: 103662. Doi: 10.1016/j.advwatres.2020.103662.
The distribution of R2 and NSE statistics across the 111 articles are shown here. These statistics reflect comparisons of SWAT simulated streamflows versus corresponding measured values for monthly, daily or sub-daily time periods. Nearly 90% of the NSE statistics and > 90% of the R2 statistics exceed 0.5 and 0.6, respectively, which are suggested thresholds for satisfactory model simulation.
The majority of the 111 SWAT studies reported “satisfactory ”performance, with a particular emphasis on peak flow comparisons. The review further revealed a need for model modifications that result in improved replication of peak and low flows, and development of an extreme flow module within an overall SWAT modelling system.
A total of 111 SWAT studies were published between 1999 and 2020, that reported extreme flow, drought, flood, or drought and flood assessments
The largest number of studies were conducted in the United States and China among represented countries in the study
This is the first review of SWAT performance for replicating hydro-climatic extremes